## Slide 1: Common Failures in the Field: Recommendations for Avoiding Downtime, Machine Damage & Injury Alison Mackey Baker Hughes, a GE Company

## Slide 2: Introduction State of the Industry Predictive Analytics Overview & Case Studies Building a Digital Asset Management Program
Agenda

## Slide 3: Introduction
Increasing capital efficiency & profitability
Decrease Operating Cost
Manage Resources
Connecting Digital
Other Benefits
Knowledge gap closure
Competitive advantages
Automation
Notes: Enhancing productivity – maximizing recovery, improving equipment reliability, identify hidden productivity gains, minimize downtime & extend asset life
Reducing Operational Complexity – issuing recommendations to decrease overall parts & labor costs, provide analysis over fleets or groupings of equipment
Improve resource utilization – inventory management, online parts ordering, increased access to information with digitized manuals

## Slide 4: State of the Industry

## Slide 5: State of the Industry
Aging Resources
Market Downturn
Data Demand
40% of O&G production comes from wells that are 25+ years old
Existing field optimization is key
Do more with less
Searching for opportunities to become more efficient
Global demand for data in every aspect
Bottom line boosts from digital
What drives demand for digital?

## Slide 6: How do we get there?
Modular
Scalable
Autonomous
No one-sized-fits-all approach
Modular does not equal complicated
Single source of truth
What data gives the most value?
Systems should REDUCE workload
Set it and forget it
Solutions should have three main characteristics…

## Slide 7: Predictive Analytics Overview

## Slide 8: Smart Compressor System
In cylinder pressure
Compressor package process Instrumentation
Hi speed DAQ
Cell Router
Integrated Controller
PLC + Edge
APM Module
+
Insights
Connectivity
Assets
Valuable insights can be derived from typical process data
In cylinder pressure data provide comprehensive compressor health
Integrated controller…Edge & Cloud functionality
In cylinder pressure measurement
Reliable and secure data transmission
Configurable based on needs
Key Features
Comprehensive health monitoring
Compressor & engine analytics
Internal pressure monitoring & analytics
Compressor digital twin – performance & compressor simulation
Monitoring & analytics through MyPlantTM platform
Providing real time insights for proactive planning
Ongoing developments…Edge analytics & optimization
Benefits
Detect, diagnose & proactively plan
Increased reliability & efficiency
Case study…temp & valve analytics have predicted several valve issues
Limits
Early detection
Detect
Closing limits
Diagnose
Failed valve

## Slide 9: Technology development
Future development…
+Bearing Performance
+Vibration
+Oil Performance
General Dashboard
Real time asset condition visibility of key comp parameters including shutdowns/alarms
Physics-Based Analytics
Provide early indication of potential issues
Discharge Temperature…potential valve issues
Stage Pressures…potential pulsation issues
Op Envelope
Real time assessment of comp performance allowing for safe operation through range of op conditions
  Flow/HP
  Rod & Crankpin Loads
  Reversals
Valve Performance
Real time assessment of valve performance & early indication/prevention of potential valve issues
HP/Flow Optimization
Maximize throughput w/advisory on capacity controls for safe operation
PV Analytics
Provide near real time assessment of overall compressor health including valve & ring leakages
Frame Vibe
Lube Oil Temp & Pressure
Oil Level
Rod Loads & Reversals
Flow & HP
RPM
Discharge Temp
Analytics (valves)
Analytics (pulsation)
Valve Performance
Maintenance
Valve & Ring Leakages
Maintenance
HP/Flow Opt

## Slide 10: myPlant Dashboard Features
Main Page
Analytics Page
Operating hours (h)
xxxx
Starts
xxxx
Starts per Week
xxxx
OPH/Start Ratio
xxxx
Analytics Notifications
xxxx
xx
xx
LB IMAP
RB IMAP
xx
IMAP Differential (%)
xx
xx
EGT min
EGT max
xx
EGT spread max (F)
xx
Oil Pressure (psig)
OK
OK
Valves & Rings
Cylinders
OK
Running Gear
Completed 1Q18!

## Slide 11
Cylinder Analytics – Discharge Temp Monitoring
This algorithm detects deviation in the cylinder discharge temperatures based on the theoretical discharge temperatures. The approach is to monitor the discharge temperatures and detect slow deviations/drifts from the theoretical temperatures. At detection the algorithm will create an alarm.
Data to be investigated
  Cylinder suction & discharge temperatures
  Cylinder suction & discharge pressures
  Engine speed
Events and analysis of trend data
  Cylinder discharge temperature is a function of stage pressure ratios, speed and suction temperatures. Increasing temperatures can be related to other issues associated with valves, piston rings and packing rings. The algorithm will monitor the actual temperatures against theoretical and will detect increasing deviations/drifts.
Indication in the Analytics Overview
    In case of an issue with the component, it will be directly indicated in the analytics overview either with a warning (yellow) or an alarm (red)
Normal: Deviation in temperature relative to baseline small & consistent over time.
Priority/Action: No action, no ticket
Warning: An abrupt change could be related to issues with leaking valve/rings, data quality or temporary sensor issues
Priority/Action: Check service history. Further monitoring recommended. Inspection on next PM interval
Trending Examples
Alarm: A clear gradual increasing drift compared to baseline.
Priority/Action: Check valve and piston rings for abnormal wear.
Analytics Overview
Actual
Baseline
Actual
Baseline
Actual
Baseline

## Slide 12: Case Studies

## Slide 13: Temperature Analytics – Unit C2000
Delta 0F
Delta 9F
Temperature Signature
Temperature Analytic
Key takeaways/observations
Data taken from Sept. 22nd to Oct. 10th
Units loss communications after Oct. 10th
1st stage #3 cylinder only cylinder to show consistently higher deltas (~9-10 F)
Anomaly observed between 1st stage cylinders

## Slide 14: Temperature Analytics – Unit C2100
Delta 0F
Delta 9F
Temperature Signature
Temperature Analytic
Key takeaways/observations
Data taken from Sept. 22nd to Oct. 10th
Units loss communications after Oct. 10th
All cylinders running normally until Oct. 5th and noticed a slight anomaly between 1st stage cylinders
Cylinder #1 showing slow trending in delta (~5F)

## Slide 15: Temperature Analytics – Unit C2200
Delta 0F
Delta 9F
Key takeaways/observations
Data taken from Sept. 22nd to Oct. 10th
Units loss communications after Oct. 10th
All cylinders running normally until Oct. 1st and noticed beginning anomaly between 1st stage cylinders
Cylinder #1 delta trending towards ~9F

## Slide 16: Valve Performance App – Unit C2000 1st Stage Cylinders
CE Suction
CE Discharge
HE Suction
HE Discharge

## Slide 17: Valve Performance App – Unit C2000 1st Stage Cylinders
CE Suction
CE Discharge
HE Suction
HE Discharge
Late closing observed for ~40% of operating time
Late closing observed for ~5% of operating time
Impact speed observed higher than C2100

## Slide 18: Valve Performance App – Unit C2100 1st Stage Cylinders
CE Suction
CE Discharge
HE Suction
HE Discharge

## Slide 19: Valve Performance App – Unit C2100 1st Stage Cylinders
CE Suction
CE Discharge
HE Suction
HE Discharge
Late closing observed for ~10% of operating time

## Slide 20: Valve Performance App – Unit C2200 1st Stage Cylinders
CE Suction
CE Discharge
HE Suction
HE Discharge

## Slide 21: Valve Performance App – Unit C2200 1st Stage Cylinders
CE Suction
CE Discharge
HE Suction
HE Discharge
Late closing observed for ~30% of operating time
Impact speed observed higher than C2100

## Slide 22: Summary of Observations from Temp & Valve Analytics
Unit | Temp Analytic | Valve App
C2000 | 1st Stage Cyl #3 deltas running ~10F consistently 1st Stage anomaly observed 100% of time | Late closing observed on CE suction for ~40% of time Late closing observed on HE discharge for ~5% of time
C2100 | 1st Stage Cyl #1 deltas running ~5F 1st Stage anomaly trending ~30% of time | Late closing observed on CE suction for ~10% of time
C2200 | 1st Stage Cyl #1 deltas trending~9F 1st Stage anomaly trending ~50% of time | Late closing observed on CE suction for ~30% of time

## Slide 23: Unit 2300
2 stage 4-throw compressor
Case Study
Discharge temperature monitoring showed sudden change in 1st stage cylinder #3 compared to corresponding cylinder #1 (see Figure 1).
Discharge Temperature - Cylinder #1
Discharge Temperature - Cylinder #3
1st stage – 2x 12” DA cylinders (cylinder 1 & 3)
2nd stage – 2x 6.25” DA cylinders (cylinders 2&4)

## Slide 24: Unit 2300
2 stage 4-throw compressor
Case Study
Delta Discharge Temperature - Cylinder #1
Delta Discharge Temperature - Cylinder #3
Customer was notified trends started diverging
Trend running below alarm/warning limits after valve reinstallation
Image of damaged valve
1st alarm - warning alarm for divergence
2nd alarm - “red” alarm reached – customer shut down and performed recommended maintenance
Confirmed bad valve & back to normal operating conditions afterward
Notes: On Oct 12th the customer was notified that cyl #1 and cyl #3 discharge temperature trends started diverging from each other. As soon as cyl #3 deviation achieved alarm limit, notification was sent to machine operator. In the following days, customer decided to shut down unit and performed unit inspection. It was found that cylinder #3 Crank End (CE) suction & discharge valves were damaged causing losses on machine performance and creating potential risk of damage to other running gear components. After new CE valves were installed, operator noticed cylinder #1 and cylinder #3 trends to converge again and running below alarm/warning limits.

## Slide 25: Summary of Valve Failure Costs
Unit | Hours of Data | Stage 1 Failed Valve Hours | Stage 2 Failed Valve Hours | Revenue Lost [$] | Notes
C2000 | 5688 | 355 | 0 | $11,921.40 | 
C2100 | 7944 | 256 | 0 | $3,681.60 | Average failure lasted 3-4 days before detected/fixed
C2200 | 5496 | 16 | 0 | $152.00 | Only 1 failure for 16 hrs
C2300 | 5544 | 648 | 143 | $11,400.00 | Stage 1 had multiple failures from 6/7 to 6/13 and 10/20 to 11/10, Stage 2 failure 01/13/18 to 01/19/2018
C2400 | 1662 | 0 | 0 | $ - | Not enough data
Unit 3 | 8976 | 4109 | 736 | $70,156.40 | Frequent overload, undetected valve failure from 5/10/17 to 10/24/17
Unit 4 | 10800 | 214 | 106 | $7,900.00 | Also failure from 7/8/16 to 2/22/17 costing $77,000 but ignored because could be other sensor/component failure
Unit 2, Unit 3, Unit 4, Unit 5 | 7032, 7728, 6120, 4320 | 0 | 0 | $- | Unit 4 one failure on 4/21 fixed in 18hr. No valve failures on other units
C-203, C-204, C-205, C-206, C-207 | 24, 1272, 168, 840, 888 | 0 | 0 | $- | Limited data (1-2 months)
C100 | 2784 | 1600 | 2328 | $57,169.60 | Two long failures (>900 hrs) contribute to the high number. Possible ongoing failed valve on stage 2 (failed 01/02/2018)

## Slide 31: Building a Digital Asset Management Program

## Slide 32: Considerations
What systems and data are being collected currently?
What would bring the most value?
What resources do you have available?
Modular, scalable solutions work best!